| 首页 |  | 产品技术参数表（Specification） | SJ00207138 |
| --- | --- | --- | --- |
| 发放单位 全质11 技术20 工艺21 质控22 生产23 供应24 物资25 家经27 客服28 出口29 财务31 研究32 外管33 成本34 市场 商研35 巴西36 成品39 空一40 空二41 空三42 钣金43 喷塑44 注塑45 两器46 管路47 模具48 筛选49 丹阳50 控制51 试制52 空四53 空五58 重庆62 |  | GWHN24C1NK1AA | 生效日期: 共 2 页 第 1 页 Page 1 of 2 |
|  | 整机成品码(Product Code)：CA15200050 Model GWHN24C1NK1AA Function COOLING HEATING Rated Voltage 220-230V~ Rated Frequency 50HZ Total Capacity (W) (High/Normal *): 7100 8000 Power Input (W) (High/Normal*) 2700 2700 Rated Input (W) (High/Normal*) 4000 3000 Rated Current (A) (High/Normal *) 23.5 16.0 Air Flow Volume (m3/h) (H/M/L)** 1100 Dehumidifying Volume (l/h) 3.0 C.O.P / EER (W/W) (High/Normal*) 2.63/2.96 Indoor unit Model of Indoor Unit GWHN24C1NK1AA/I Fan Motor Speed (r/min) (H/M/L) 1260/1170/1080 Output of Fan Motor (w) 26 Input of Heater (w) —— Fan Motor Capacitor (uF) 3 Fan Motor RLA(A) 0.40 Fan Type-Piece Cross flow fan – 1 Diameter-Length (mm) φ106 X 890 Evaporator Aluminum fin-copper tube Pipe Diameter (mm) Φ7 Row-Fin Gap(mm) 2-1.4 Coil length (l) x height (H) x coil width (L) 901.6X25.4X381 Swing Motor Model MP24GA Output of Swing Motor (W) 2 Fuse (A) PCB 3.15A Transformer 0.4/0.1A Sound Pressure Level dB (A) (H/M/L) 46/44/41 Sound Power Level dB (A) (H/M/L)*** 56/54/51 Dimension (W/D/H)( mm) 1178 X326X227 Dimension of Package (W/D/H)( mm) 1265X417X333 Net Weight /Gross Weight (kg) 17.5/24 |
| 会 签 | 编 制 | 刘鲲 | 20051207 |  |  |  |  |  |
| 黄德生 | 审 核 | 秦宪 | 20051207 |  |  |  |  |  |
|  | 标 准 化 | 盛莹 | 20051207 |  |  |  |  |  |
| S122. DOC | 审 定 | 张远忠 | 20051207 | 标 记 | 处 数 | 更 改 文 件 号 | 签 名 | 日期 |

| 副页 |  | 产品技术参数表(Specification) | SJ00207138 |
| --- | --- | --- | --- |
|  |  | GWHN24C1NK1AA | 生效日期: Page 2 of 2 |
|  | Outdoor unit Model of Outdoor Unit GWHN24C1NK1AA/O Compressor Model LH48VBAC Compressor Type Hermetic motor compressor L.R.A. (A) 63 Compressor RLA(A) 12.3 Compressor Power Input(W) 2660 Overload Protector Internal Inherent Protector Throttling Method Capillary Starting Method Capacitor Working Temp Range (℃) -5≤T≤43 Condenser Aluminum fin-copper tube Pipe Diameter (mm) Φ9.52 Rows-Fin Gap(mm) 2-1.4 Coil length (l) x height (H) x coil width (L) 730.5X813X44 Fan Motor Speed (rpm) (H/M/L)** 815 Output of Fan Motor (W) 60 Fan Motor RLA(A) 1.0 Fan Motor Capacitor (uF) 3.5 Air Flow Volume of Outdoor Unit ---- Fan Type-Piece Axial fan –1 Fan Diameter (mm) Φ460 Defrosting Method Auto defrost Climate Type T1 Isolation I Moisture Protection IP24 Permissible Excessive Operating Pressure for the Discharge Side(MPa) 2.5 Permissible Excessive Operating Pressure for the Suction Side(MPa) 0.6 Sound Pressure Level dB (A) (H/M/L) 58 Sound Power Level dB (A) (H/M/L) 68 Dimension (W/D/H)( mm) 1006X340X847 Dimension of Package (W/D/H)( mm) 1100X450X905 Net Weight /Gross Weight (kg) 72/77 Refrigerant Charge (kg) R22 / 2.55kg Connection Pipe Length (m) 5 Outer Diameter Liquid Pipe (mm) Φ9.52(3/8”) Gas Pipe (mm) Φ16(5/8”) Max Distance Height (m) 15 Length (m) 30 |
|  | 编 制 | 刘鲲 | 20051207 |  |  |  |  |  |
| S122. DOC | 审 核 | 秦宪 | 20051207 | 标 记 | 处 数 | 更 改 文 件 号 | 签 名 | 日期 |